ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ÚÂÄ¿  ÚÂÄÄ¿ ÚÂÄ¿ ¿ ÚÂÄÄ¿ ÚÂÄÄ¿ ÚÄÂÂÄ¿ Ú¿  ¿
                ÃÅÄÁ¿ ÃÅÄ   Ã´ ³ ³ ÃÅÄ   ÃÅÄÄ´   Ã´   ÃÅÄÄ´
                ÀÁÄÄÙ ÀÁÄÄÙ ÀÙ ÀÄÙ ÀÁÄÄÙ ÀÙ  Ù   ÀÙ   ÀÙ  Ù
                           ÚÄÂÂÄ¿ Ú¿  ¿ ÚÂÄÄ¿
                             Ã´   ÃÅÄÄ´ ÃÅÄ
                             ÀÙ   ÀÙ  Ù ÀÁÄÄÙ
                 ÚÂÄÄ¿ ÚÂÄÄ¿ ÚÂÄÂÄ¿ ÚÂÄÄ¿ Ú¿ ÚÂÄ¿ ¿ ÚÂÄÄ¿
                 ÃÅÄÂÙ ÃÅÄ   Ã´ ³ ³ ÃÅÄÄ´ Ã´ Ã´ ³ ³ ÀÁÄÂ¿
                 ÀÙ À  ÀÁÄÄÙ ÀÙ Ù Ù ÀÙ  Ù ÀÙ ÀÙ ÀÄÙ ÀÄÄÁÙ
                                 Magazine
                       This phile dated 06/22/1994

                            Volume 3, Issue 4

                  You can always find BTR on PsychoTron BBS
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 I found this and just put it in, it's good.

 -------------------------------------------

You remember the little "bug" installed on the bad guys car in the James Bond
 flicks that allowed Bond to follow the car from a distance? Well this file is
 a tutorial on them.
 
 First, they do exist, I've built my own, but even the best commercial units
 intended for law enforcement purposes wont do what the Bond model purports
 to do, that is, give a printout on a moving map showing the route driven by
 the bug toter.
 
 The basics of the unit are the transmitter, which is about the size of
 a pack of cigarettes and is held on via a magnet. And a receiver, using 2
 identical antennas, coupled to a center zero meter which gives a heading
 towards the transmitter. More on these later.
 
 The receiver/display unit is used by pilots, amateur radio operators, and
 law enforcement and security personnel to track the movements of the
 transmitter
 usually at short ranges, the civil air patrol uses these units to find
 downed aircraft by tracking the emergency beacon, activated by the
 impact of the crash. Amateurs play "hunt the fox" to keep illegal transmitters
 out of the ham bands. Law enforcement personnel track the movement of people,
 drugs, and weapons by attaching a transmitter to the object (or suspect's
 car) to be followed.
 
 The transmitter is usually a small VHF or UHF battery operated package
 dangling a 19" flexible antenna (about the thickness of piano wire). The
 transmitter does not "beep" per say, but transmits a continual carrier.
 The FBI uses 167.xxx mhz for theirs and the local DA uses the intercounty
 police freq of 155.37. I have seen military models that use 149.xxx mhz
 around here (air force).
 
 Now the receiver:
 Two identical antennas mounted on the chase vehicle (usually magnetic mounts)
 feed a pair of PIN diodes that feed a phase detector which samples the
 receiver's IF output. When the received signal is directly in front of you,
 signals arrive at exactly the same time at each antenna. This is calibrated to
 read center 0 on the meter. (Incidentally the unit can't tell if the signal is
 in front or in back of you, so the need to make sure you follow the subject
 reasonably closely is apparent). If the bug travels say to 10 o'clock on the
 compass rose, the needle will swing to 4 o'clock on the meter. The object here
 is to always drive towards zero and you follow the bug in the most direct
 direction. With a little practice,you can follow a subject on an adjcent
 street without loosing him.
 The meter swings because the signal arrives later at one antenna than the
 other, causing a voltage change in the phase detector (an Exar Radio-teletype
 decoder chip in my model).
 
 Some recent units ive seen have Light emitting diodes in a 360 degree circle
 and use 4 antennas. This gives you full circle detection capabilitys as the
 phase between pairs of antennas is calculated also.
 
 Now, prevention:
 The easiest way to detect if you've been planted with one of these little
 transmitters, is to walk around the car or whatever with a portable frequency
 counter and check for an alien RF signal. This is also the recommended
 method to de-bug your home. A small freq counter with 1.2 ghz capabilitys
 sells for around $100. today. If you do find a transmitter, have fun with it.
 Stick it on a train heading out of town, a Greyhound bus, or a over the road
 tractor-trailer rig....my favorite is to stick it on one of their own
 vehicles and watch them chase themselves....hehehe.
 



-+\+-
A BTR production
All rights lost.

-rk